HUGHES

AND ASSOCIATES, INCORPORATED

11728 LINN AVE NE

ALBUQUERQUE, NM 87123

(505) 292-9770

FAX (505) 292-8405

NM LICENSE #28954

SITE-SPECIFIC ERECTION PLAN FOR:

ARMY AVIATION SUPPORT FACILITY

1. Sequence of erection activity:  Zone A-B, Upper Roof A/B, Low Roof Area, C/D/E, to upper C/D/E unheated storage building. Grids 1-5 braced depending on metal building erection plans. Same with wash rack, canopy and guard house. All this depends on steel deliveries, fabrication and concrete issues.

A. Material deliveries: As notified per fabricator, General Contractor, with the

understanding material should be sent out with the sequence of erection in

mind.  Deck and steel are to be broken down or marked by zone.

B. Material staging: As provided by General Contractor off of ground dunage

C. Coordination with other trades: With General Contractors directions

2. Description of the crane:

A. Site Preparation: Level as possible for cranes and forklift operation

B. Path for overhead loads: No personnel allowed under erection area except

for erection crew.

C. Critical lifts. No lifts will occur more than 70% of crane capacity.

D. What type of rigging will be used: Steel and nylon slings, all tagged of

capacity and checked daily. Qualified rigger/competent person will inspect

all rigging daily and eliminate all rigging that is not tagged or not in good

condition.

E. Power lines: Moved, shut off or insulated.

3. Description of steel erection activities and procedures:

A. Stability consideration requiring temporary bracing and guying: Done as

needed with direction of competent foreman.

B. Erection bridging terminus point: Will be secured before any loads are placed

on joist.

C. Anchor bolts? Any repairs? If so, get documents that were given from

structural engineer. Written notice to commence must be received before

start of erection, notice must state concrete has reached 75% of strength and

anchor bolt survey including any repairs made to bolts.

D. Columns and beams: (including joist and purlins) includes all

Procedure is to set columns, plumb up, box in iron or joist to steel or masonry

to support structure before moving on.

E. Connections: Weld or bolt as required.

F. Decking: Controlled Decking Zone. A controlled decking zone will be

established in that area of the structure over 15 and up to 30 feet above a lower

level where metal decking is initially being installed and forms the leading

edge of a work area. Tie off is required by contractor above 6 feet. We will use

tie off cables, retractables, etc…… to comply with this.

G. Ornamental and miscellaneous iron:

4. Fall protection: Each employee engaged in steel erection activity who is on a

walking/working surface with an unprotected side or edge more than 6 feet above a

lower level shall be protected from fall hazards by guardrail systems, personal fall

arrest systems,positioning device systems or fall restraint systems. We use a Stanchion

post and rope system that has been certified (certification in book). Stanchion post are

set on carrier beams and the use of the beam and/or tie off cables are used to cut the

load from crane.

5. Falling object protection: All materials, equipment, and tools which are not in use

while aloft, shall be secured against accidental displacement. The controlling

contractor shall bar other construction processes below steel erection unless overhead

protection for the employees below is provided.

6. Description of special procedures required for hazardous non-routine tasks: At

this point , there is no non-routine tasks but each task will be regarded as hazardous

and safety will always be our objective.

7. Certifications for each employee: All of our employees have all their certifications to

perform their duties. Most employees have their cards on them. Once we determine

who is going to be on the jobsite we will provide copies for your files.

8. List of qualified and competent persons: A list will be given once crew is

determined.

9. If an accident does occur call 911:

ARMY AVIATION SUPPORT FACILITY   	GENERAL CONTRACTOR

7001 HUEY ROAD		                              PCL CONSTRUCTION

SANTA FE, NM 87507

SIGNATURES

_________________________________ Hughes And Associates, Inc.

_________________________________ Foreman for Hughes And Associates, Inc.

__________________________________General Contractor’s Representative